## Slide 1: Module 5: Clause 8 – Operation
AS9100 Lead Auditor Training | Day 2 AM

## Slide 2: Clause 8 Overview
Largest clause: core of product/service delivery
Must audit with high sampling and strong risk-based focus

## Slide 3: 8.1 Operational Planning & Control
Plan product realization with risk-based thinking
Controls, resources, verification, traceability
Audit for missing control plans or inconsistent methods

## Slide 4: 8.1.1 Operational Risk Management
Unique to aerospace: bullet list of risks
Include: capacity, capability, supply chain, human factors
Audit: Show risk response plan per major change

## Slide 5: 8.2 Requirements for Products & Services
Customer needs must be defined, reviewed, confirmed
Contract Review: Explicit clauses, flowdowns, capabilities
Audit test: Compare PO to internal spec—any gaps?

## Slide 6: 8.3 Design & Development
Can be excluded only if NO design responsibility
Includes planning, inputs, controls, outputs, changes
Audit: FMEA, DVP&R, traceable inputs, change records

## Slide 7: 8.3 Audit Focus
Design inputs linked to requirements
Verification vs validation evidence
Change control: impact analysis, approval trail

## Slide 8: 8.4 Control of External Providers
Risk-based supplier control
Approval, monitoring, re-evaluation
Audit: FAI from sub-tier, e-cert integrity, nonconformances

## Slide 9: 8.5 Production & Service Provision
Includes special processes, traveler flow, job control
Marking, preservation, traceability
Audit clue: expired material, uncontrolled rework

## Slide 10: 8.5.1 Control of Production
Use of documented work instructions, criteria, qualified staff
FOD control, accountable labeling, maintenance
Audit: Walk production line for unauthorized processes

## Slide 11: 8.5.1.1 Prevention of FOD
Defined FOD zones, controls, inspections
Audit: Employee FOD awareness, recent incident log

## Slide 12: 8.5.1.2 Control of Production Tools
Tooling maintained, calibrated if measuring, traceable
Audit: Review log of tool life, assigned ownership

## Slide 13: 8.5.1.3 Control of Temporary Means
Masking, simulation, temporary bypass = controlled
Audit: Marked clearly, records updated post-removal

## Slide 14: 8.5.2 Identification and Traceability
Unique part IDs, serialized lots, traveler integrity
Audit: Does trace link to FAI, CoC, and shipment record?

## Slide 15: 8.5.3 Property Belonging to Customers
Must be identified, verified, protected
Audit: Evidence of reporting damage or loss?

## Slide 16: 8.5.4 Preservation
Handling, packaging, storage, protection
Audit: Visual walk to validate controls in place

## Slide 17: 8.5.5 Post-Delivery Activities
Install, maintain, warranty, recalls
Audit: Post-shipment issue log reviewed regularly?

## Slide 18: 8.5.6 Control of Changes
Change to production = re-validate risk and impact
Audit: Who can approve, what’s the workflow?

## Slide 19: 8.6 Release of Products & Services
Documented evidence of conformity required
Audit: Lot release tied to what checks, who signs?

## Slide 20: 8.7 Control of Nonconforming Outputs
ID, contain, disposition, escalate
Audit: Review NCRs, escapes, use of rework paths

## Slide 21: Clause 8 Quiz & Summary
1. Clause covering FOD?
2. Required evidence for product release?
3. What is required for tooling control?
4. How is post-delivery feedback captured?
5. One example of temporary means?